## Slide 1
ENGINEERING INNOVATION • EDGE-AI • NDT SCREENING
THERMOACOUSTIX: EDGE-BASED ANOMALY DETECTION SYSTEM
A low-cost automated vibration-based material screening prototype
FROM IMPACT TO INSIGHT
Presented by TEAM VOLTAGE MAFIA
Submitted By:
SAKSHAM DHAWAN (26BVD0024)
PATNALA SUBHAOM KUMAR PATRO (26BEC0268)
AYAAN GARG (26BEC0472)
VIT Vellore • B.Tech ECE AND VLSI
VIT VELLORE • B.TECH ECE AND VLSI 01 / 18

## Slide 2
01 • NON-VISIBLE DIFFERENCES
THE PROBLEM WE ARE SOLVING
Identical outside. Mechanically different inside.
Defects, damage and material variation can hide beneath a normal surface — across brackets, structural parts, machine components and glass samples.
HUMAN
HAMMER
EAR / EYE
SUBJECTIVE
CONTROLLED IMPACT
ADXL345
FFT + REFERENCE
DECISION
TRADITIONAL
OUR APPROACH
COST • HUMAN VARIABILITY • ENVIRONMENT • LIMITED AUTOMATION
How can repeatable excitation + digital vibration features reveal deviation from a known reference?
VIT VELLORE • B.TECH ECE AND VLSI 02 / 18

## Slide 3
02 • PHYSICAL RESPONSE → DIGITAL EVIDENCE
OUR CORE IDEA
MATERIAL
SERVO STRIKE
VIBRATION
ADXL345
RAW SIGNAL
FFT
REFERENCE
ANOMALY
Every material answers an impact with a characteristic vibration signature.
“Converting a physical vibration response into measurable digital information.”
Repeatable excitation makes responses comparable. Frequency features make them computable.
VIT VELLORE • B.TECH ECE AND VLSI 03 / 18

## Slide 4
03 • ESP32 AS THE CENTRAL BRAIN
SYSTEM ARCHITECTURE
ESP32
CONTROL • ACQUIRE
COMMUNICATE
POTENTIOMETER
profile
SERVO
striker
LCD
status
DHT11
T + RH
PYTHON
advanced DSP
ADXL345
vibration
FFT →
DECISION
SENSORS / CONTEXT
ACTUATION / OUTPUT
Actuator → Material → ADXL345 → ESP32 / Python → FFT → Decision
VIT VELLORE • B.TECH ECE AND VLSI 04 / 18

## Slide 5
04 • AUTOMATED TEST SEQUENCE
HOW THE SYSTEM WORKS
01
LOAD SAMPLE
02
PRESENCE CHECK
03
SELECT PROFILE
04
VERIFY CHAMBER
05
SERVO STRIKE
06
CAPTURE VIBRATION
07
LOG ENVIRONMENT
08
FILTER + WINDOW
09
FFT
10
EXTRACT FEATURES
11
COMPARE BASELINE
12
CHECK TOLERANCE
13
DISPLAY + ALERT
VIT VELLORE • B.TECH ECE AND VLSI 05 / 18

## Slide 6
05 • COORDINATION, NOT JUST COMPUTATION
ESP32 — THE BRAIN
ESP32
COORDINATED
INSPECTION
SENSOR READING
SERVO CONTROL
SAFETY MONITORING
USER INPUT
LCD
PYTHON LINK
TEST SEQUENCING
“Transforms components into a coordinated automated inspection system.”
IoT • industrial automation • smart monitoring • robotics • sensor networks
VIT VELLORE • B.TECH ECE AND VLSI 06 / 18

## Slide 7
06 • REPEATABILITY MEETS MEASUREMENT
CONTROLLED EXCITATION & VIBRATION SENSING
SERVO STRIKER
Repeatable mechanical impact
• reduces manual variation
• automates testing
• improves comparability
ROBOTICS • ACTUATION • POSITIONING
ADXL345
Time-domain acceleration response
• transient amplitude
• oscillation behaviour
• decay characteristics
CONDITION MONITORING • MOTION • VIBRATION
SERVO → CONTROLLED IMPACT → MATERIAL → VIBRATION → ADXL345
VIT VELLORE • B.TECH ECE AND VLSI 07 / 18

## Slide 8
07 • TIME DOMAIN → FREQUENCY DOMAIN
FFT — THE FREQUENCY SIGNATURE
TIME DOMAIN
When and how vibration changes
FREQUENCY DOMAIN
Which frequencies — and their strengths
FEATURES dominant frequency • peak amplitude • spectral energy • ratios • band energy • decay
FFT extracts features. It does not, by itself, decide defect presence.
VIT VELLORE • B.TECH ECE AND VLSI 08 / 18

## Slide 9
08 • SIGNAL PROCESSING PIPELINE
FROM RAW ACCELERATION TO ANOMALY SCORE
Δf = Fs / N
Nyquist: Fs > 2 × Fmax
Sampling rate must capture the frequency range of interest.
Sampling digitises • filtering removes noise • windowing reduces leakage • spectrum exposes strengths • comparison creates a threshold or model-based decision
VIT VELLORE • B.TECH ECE AND VLSI 09 / 18

## Slide 10
09 • CONDITION-AWARE MEASUREMENT
WHY DHT11?
VIBRATION DATA
TEMPERATURE
HUMIDITY
CONDITION-AWARE
DATASET
CALIBRATION /
COMPENSATION MODEL
DHT11 temperature + humidity
Context aids future calibration — it does not automatically remove false positives.
VIT VELLORE • B.TECH ECE AND VLSI 10 / 18

## Slide 11
10 • HARDWARE → FUNCTION → ENGINEERING VALUE
EVERY COMPONENT HAS A PURPOSE
ESP32
Central control + communication
IoT / automation
ADXL345
Vibration measurement
Condition monitoring
Servo motor
Controlled excitation
Robotics / actuation
Potentiometer
Profile selection
Analogue interface
LCD
Status, result, alert
Human–machine interface
DHT11
T, RH and pressure context
Environmental sensing
VIT VELLORE • B.TECH ECE AND VLSI 11 / 18

## Slide 12
11 • THE INNOVATION IS THE INTEGRATION
WHAT MAKES OUR SYSTEM INNOVATIVE?
01
CONTROLLED EXCITATION
Automated, repeatable impact
02
DIGITAL SIGNATURE
Physical response becomes data
03
FFT ANALYSIS
Comparable frequency features
04
ENVIRONMENTAL CONTEXT
Conditions recorded per test
05
EMBEDDED AUTOMATION
ESP32 coordinates the system
06
SAFETY INTERLOCKS
Physical conditions gate testing
MECHANICS + SENSORS + EMBEDDED CONTROL + DSP + CONTEXT + ANOMALY DETECTION
VIT VELLORE • B.TECH ECE AND VLSI 12 / 18

## Slide 13
12 • BUILT FOR ACCESSIBLE EXPERIMENTATION
BENEFITS & ADVANTAGES
LOW COST
Affordable prototype hardware
AUTOMATED
Less manual intervention
REPEATABLE
Controlled excitation
FAST
Rapid capture + processing
PORTABLE
Compact desktop potential
DATA-DRIVEN
Measurable signatures
SCALABLE
Upgradeable sensing + AI
ECE + EMBEDDED SYSTEMS + SENSORS + CONTROL + DSP + FFT + AI / ML
VIT VELLORE • B.TECH ECE AND VLSI 13 / 18

## Slide 14
13 • FROM LAB BENCH TO SMART FACTORY
REAL-WORLD APPLICATIONS
01 Manufacturing quality screening
02 Machine condition monitoring
03 Structural response research
04 Material deviation screening
05 Small workshops & labs
06 Educational NDT demonstrations
07 Future smart-factory integration
EXPERIMENTAL SCREENING PLATFORM — NOT A CERTIFIED REPLACEMENT FOR INDUSTRIAL NDT.
VIT VELLORE • B.TECH ECE AND VLSI 14 / 18

## Slide 15
14 • PROTOTYPE
PROTOTYPE PHOTO
VIT VELLORE • B.TECH ECE AND VLSI 15 / 18
PROTOTYPE CREATION!!

## Slide 16
15 • RESULTS
RESULTS
VIT VELLORE • B.TECH ECE AND VLSI 16 / 18
WHEN THE HAMMER HITS AN OBJECT/METAL, IT DETECTS THE ANOMALY AND INTERNAL DEFECTS PRESENT. THESE PHOTOS SHOWS THE NO OF SAMPLES AND THE FFT GRAPH CONFIGURED DURING THE HAMMER HIT.

## Slide 17
16 • RESULTS
RESULTS
VIT VELLORE • B.TECH ECE AND VLSI 17 / 18
WHEN THE HAMMER DOESN’T HIT ANY KIND OF OBJECT OR METAL, IT DOES NOT DETECT ANY DEFECTS, THUS, SHOWING A STRAIGHT GRAPH WITH VERY FEW DISTURBANCES OR ANOMALY DETECTIONS.

## Slide 18
17 • FOUR-LEVEL ROADMAP
FROM PROTOTYPE TO SMART INSPECTION
LEVEL 1
BETTER SENSING
High-bandwidth accelerometers • piezo • force sensing • isolation
LEVEL 2
BETTER DSP
Digital filters • wavelets • resonance tracking • optimised FFT
LEVEL 3
REAL MACHINE LEARNING
Python training → optimise → TinyML → ESP32 edge inference
LEVEL 4
INDUSTRIAL SCALE
Calibrated impact • multi-sensor line • database • dashboard
We are not simply measuring vibration. We are turning vibration into information — and information into a decision.
FROM IMPACT TO INSIGHT.
VIT VELLORE • B.TECH ECE AND VLSI 18 / 18